## Slide 1: Quarrying
Dump Trucks, Wheel Loaders, Bulldozers
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Engine | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Transmission | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -
Hydraulics / Steering | SAE 10W TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 10W ** | - | -
Final Drive | SAE 50 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 50W ** | - | -
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL

## Slide 2: Quarrying
Drill Rigs
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Engine | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Transmission | SAE 50 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 50W ** | - | -
Compressor | DIN 51506 VDL | Oxidation stability Reduced deposits Long drain intervals | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn
Thread compound | NLGI 1 | Solid lubricants Water tolerance High and low temperature capability Chemical corrosion resistance | PETRONAS Grease Li AS | - | 
Vertical bearing | NLGI 2 EP | Extreme high load Water tolerance High and low temperature capability | - | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220
Slewing ring | NLGI 2 EP | Extreme high load capability Water tolerance Solid lubricants | - | - | PETRONAS Grease MG HL
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Pneumatic drill head | ISO VG 100 or 150 DIN 51524 Part III | Water separability Anti-wear Rust and corrosion protection | PETRONAS ATO | - | -

## Slide 3: Crushing
Jaw Crusher (Primary Crusher)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Plain Bearings / Roller bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 4: Crushing
Cone Crusher (Secondary Crusher)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Plain Bearings | AGMA 4EP | High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Spider bush bearing (Grease) | NLGI 2 | High load capability High and low temperature handling Mechanical stability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Spider bush bearing (Oil) | AGMA 4-7EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL series | PETRONAS Gear Syn PAO
Gearbox / Reducer | AGMA 4EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 5: Crushing
Gyratory Crusher (Secondary Crusher)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Plain Bearings | AGMA 4EP | High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Spider bush bearing (Grease) | NLGI 2 | High load capability High and low temperature handling Mechanical stability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Spider bush bearing (Oil) | AGMA 4-7EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Gearbox / Reducer | AGMA 4EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 6: Crushing
Impact Crusher (Secondary Crusher)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Plain Bearings | AGMA 4EP | High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Spider bush bearing (Grease) | NLGI 2 | High load capability High and low temperature handling Mechanical stability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Spider bush bearing (Oil) | AGMA 4-7EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Gearbox / Reducer | AGMA 4EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 7: Crushing
Breaker Screen / Feeders
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease CaSx
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 8: Storage
Stacker / Re-claimer
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption | - | PETRONAS Grease LiCa TMG | 
Cables | OIPEEC | Core penetration Adhesive characteristics Elasticity Rust and corrosion protection | PETRONAS Grease LiCa GEP 2.5 | - | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Chains | ISO VG 220 Cincinnati Machine Spec | Tackiness Rust and corrosion protection Lubricity | PETRONAS Slideway | - | -

## Slide 9: Storage
Collectors (Re-claimer)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Open Gears | AGMA 251.01 FZG US Steel | Pumpability Adhesive characteristics Extreme pressure Low consumption |  | PETRONAS Grease LiCa TMG | 
Cables | OIPEEC | Core penetration Adhesive characteristics Elasticity Rust and corrosion protection | PETRONAS Grease LiCa GEP 2.5 | - | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Chains | ISO VG 220 Cincinnati Machine Spec | Tackiness Rust and corrosion protection Lubricity | PETRONAS Slideway | - | -

## Slide 10: Milling
Vertical Mill
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Electric Motor - Plain Bearings | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Mill Trunnion bearings | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Mill Bearing / Worm Gear | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Gear Syn PAG
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 11: Milling
Horizontal Mill
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Electric Motor (Oil) | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Plain Bearings | ISO VG Range | High load capability Low foaming tendencies Water separability | PETRONAS Circula series | - | PETRONAS Circula Syn series
Slipper pad bearing (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Slipper pad bearing (Oil) | ISO VG Range | High load capability Water tolerance Long life | PETRONAS Circula series | - | PETRONAS Circula Syn
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 12: Milling
Homogenizer
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Compressors | DIN 51506 VDL | Oxidation stability Reduced deposits Long drain intervals | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn
Blowers | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Fans (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Fans - Plain Bearings | ISO VG Range | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Circula |  | PETRONAS Circula Syn
Plummer block bearing (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease CaSX
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 13: Firing
Cyclone (preheater to kiln)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Separator Shaft Bearings | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Compressors | DIN 51506 VDL | Oxidation stability Reduced deposits Long drain intervals | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn
Fan Bearings (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | 
Fan Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Damper / Actuator valves (flue gas line) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | 

## Slide 14: Firing
Fine fuel feeder (coal or solid waste)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 15: Firing
Kiln
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Girth Gear | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption |  | PETRONAS Grease LiCa TMG | 
Thrust Bearings | ISO VG 1000 | Lubricity High load capability Oxidation resistance Anti-wear | PETRONAS Circula 1000 | - | PETRONAS Circula Syn 1000
Kiln Support Roller Bearings | ISO VG 1000 | Lubricity High load capability Oxidation resistance Anti-wear | PETRONAS Circula 1000 | - | PETRONAS Circula Syn 1000
Auxiliary Diesel Engine | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Auxiliary Reducers | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor – Bearings (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Electric Motor Bearings (Oil) | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Circula series | - | PETRONAS Circula Syn
Continued on next slide

## Slide 16: Firing
Kiln
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Drive Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Couplings | NLGI 1 AGMA CG 1 and 2 | Low oil bleed Oxidation stability Resistance to centrifugal force | PETRONAS Grease Li 2 | PETRONAS Grease PE HS | -
Live Ring |  |  | No Product / Graphite Powder |  | 

## Slide 17: Clinker Cooling
Grate Cooler
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Fan Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | PETRONAS Grease Lix Syn 2/100
Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Chains (Grid) | ISO VG 220 Cincinnati Machine Spec | Tackiness Rust and corrosion protection Lubricity High flash point | No Product / High temperature chain lubricant |  | 
Sprocket bearing | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO

## Slide 18: Clinker Cooling
Screen
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220

## Slide 19: Cement Milling
Roller Press (Pre-Milling)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Press bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Press bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 20: Cement Milling
Vertical Roller Mill
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Mill Bearing (Oil) | ISO VG 680 PAG | High load capability High temperature handling Anti-wear |  |  | PETRONAS Gear Syn PAG 680
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Electric Motor - Plain Bearings | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Mill Bearing (Grease) | NLGI 2 | High load capability High and low temperature handling Mechanical stability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 21: Cement Milling
Horizontal Ball Mill
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Plain Bearings | ISO VG Range | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Circula series | - | PETRONAS Circula Syn
Slipper pad bearing (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Slipper pad bearing (Oil) | ISO VG Range | High load capability Water tolerance Long life | PETRONAS Circula series | - | PETRONAS Circula Syn
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Electric Motor (Oil) | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Circula Syn
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO

## Slide 22: Packing
Bag Filling
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Compressors | DIN 51506 VDL | Oxidation stability Reduced deposits Long drain intervals | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn
Blowers | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Blowers /Gears | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO

## Slide 23: Packing
Palletising
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Plummer block bearing (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Slide way grease | NLGI 2 EP | High load Solid lubricants Adhesive properties | - Petronas Grease LiX MEP | PETRONAS Grease LiCa MG HL | -
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 24: Transfers
Conveyors
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Coupling | NLGI 1 AGMA CG 1 and 2 | Low oil bleed Oxidation stability Resistance to centrifugal force | PETRONAS Grease Li 2 | PETRONAS Grease PE HS | -
Idler roller bearings |  |  | Filled for life - special low viscosity grease (contact OEM for initial fill) |  | 

## Slide 25: Transfers
Blowers
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Blowers | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 26: Transfers
Bucket Elevators
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Plummer block bearing (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease CaSX
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO

## Slide 27: Transfers
Screw Conveyors
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Plummer block bearing (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease CaSX
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO

## Slide 28: Coal Plant
Coal Tippler
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Plummer block bearing (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption |  | PETRONAS Grease LiCa TMG | 
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO

## Slide 29: Coal Plant
Milling
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Mill trunion bearings | AGMA 1-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Mill Bearing | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Fans (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption |  | PETRONAS Grease LiCa TMG | 
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Electric Motor - Plain Bearings | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Gearbox / Reducer | AGMA 1-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Fans - Plain Bearings | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn

## Slide 30: General
Blowers
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSx | PETRONAS Grease LiX Syn 2/220
Gearbox / Reducer / Bearings (Oil) | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 31: General
Pumps
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Oil) | ISO VG 68 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease LiX 2/170) | PETRONAS Grease LiX Syn 2/220
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 32: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Air compressor | 51506-VDL | Oxidation stability Good air release Foam tendencies | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Air Compressors

## Slide 33: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Diesel Engine Oil | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gas Turbine | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Gearbox / Reducer | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Back Up Generators - Diesel & Gas Turbine

## Slide 34: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Cutting fluids |  | High emulsion stability Excellent lubricity and anti-weld Anti-rust, anti-corrosion Anti-sludge Anti-bacterial | Mecafluid SM 59** | Mecafluid S 2006** | -
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Hydraulics | ISO VG range HM specification | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Slide way oils | ISO VG 68 and 220 Cincinnati Machine Spec | Pumpability and sprayability Adhesive characteristics Extreme pressure | PETRONAS Slideway | - | -
Machinery Workshops