## Slide 1: Coal Yard - Transport
Coal Tippler
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Plummer block bearing (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption | - | PETRONAS Grease LiCa TMG | 
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO

## Slide 2: Coal Yard - Transport
Dump Truck, Wheel Loaders, Front End Loaders
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Converter | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 | - | -
Engine | Engine Oil 15W40 / 10W40 | Excessive dust Long periods of work Maintenance in the field | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Final Drive | SAE 50 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 ** | - | -
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Hydraulics / Steering | SAE 10W TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 10W | - | -
Transmission | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -

## Slide 3: Coal Yard - Transfers
Stacker / Reclaimer
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption | - | PETRONAS Grease LiCa TMG | 
Cables | OIPEEC | Core penetration Adhesive characteristics Elasticity Rust and corrosion protection | PETRONAS Grease LiCa GEP 2.5 | - | -
Hydraulics (Stationary) | ISO VG 46 / 68 | High viscosity index Water and dust tolerance Water separability | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Slewing Ring Bearing | NLGI 2 | Extreme load White solids Thermal and oxidation stability | - | -PETRONAS Grease LiCa HL | PETRONAS Grease LiCa XHL
Reclaimer Chains | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease LiX EP | PETRONAS Grease LiCa Semi Syn | PETRONAS Grease LiX Syn 2/460

## Slide 4: Coal Yard - Storage
Silos and stock piles
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gear drives | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Hydraulics (stationary) | ISO VG 46 / 68 High viscosity index | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 5: Coal Yard - Transfers
Feeders
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption | - | PETRONAS Grease LiCa | 
Coupling (Grease) | NLGI 1 AGMA CG 1 and 2 | Low oil bleed Oxidation stability Resistance to centrifugal force | PETRONAS Grease Li 2 | PETRONAS Grease PE HS | -
Coupling (oil) | ISO VG 46 | Oxidation stability Good air release Low foaming tendencies | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Hydraulics (stationary) | ISO VG 46 / 68 | High viscosity index Water and dust tolerance Water separability | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Reclaimer Chains | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460

## Slide 6: Coal Yard - Crushing
Crusher
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Hydraulics (Stationary) | ISO VG 46 / 68 High viscosity index | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 7: Coal Yard - Transfers
Conveyors / Handlers
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Coupling (Oil) | ISO VG 46 | Oxidation stability Good air release Low foaming tendencies | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Coupling (Grease) | NLGI 1 AGMA 1 and 3 | Low oil bleed Oxidation stability Resistance to centrifugal force | PETRONAS Grease Li 2 | PETRONAS Grease PE HS | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Hydraulics (Stationary) | ISO VG 46 / 68 High viscosity index | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption |  | PETRONAS Grease LiCa TMG | 
Conveyor Back stop | NLGI 2 |  | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 8: Coal Pulverising
Pulveriser (Vertical)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Grease points | NLGI 2 EP Solid lubricants | Water tolerance High load capability Shock loading | PETRONAS Grease LiX EP 2/380 | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Bearings (Grease) | NLGI 2 EP | High load capability Extreme water tolerance Long life | - | - | PETRONAS Grease LiX Syn 1/1500
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Hydraulics (stationary) | ISO VG 46 / 68 High viscosity index | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 9: Coal Pulverising
Ball Mill / Tube Mill
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Thrust Bearing | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption | - | PETRONAS Grease LiCa TMG | -
Bearings (Grease) | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Coupling (grease) | NLGI 1 AGMA 1 and 3 | Low oil bleed Oxidation stability Resistance to centrifugal force | PETRONAS Grease Li 2 | PETRONAS Grease PE HS | -
Electric Motor Bearings (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Electric Motor Bearings (Oil) | ISO VG 32 or 46 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460

## Slide 10: Steam Generation Plant
Boiler
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Dampers | NLGI 2 EP | Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Pressure relief valves | NLGI 2 EP Solid lubricants (white) | High temperature Long life | - | PETRONAS Grease LiX MEP | 

## Slide 11: Steam Generation Plant
Feed water & Condensate Pumps
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Turbine Drive | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Bearings (Grease) | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSx | PETRONAS Grease LiX Syn 2/220
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer (Variable Speed) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 | Petronas Grease CaSx | PETRONAS Grease LiX Syn 2/220

## Slide 12: Steam Generation Plant
Soot Blower
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Gearbox / Reducer (Grease) | NLGI 2 EP | High temperature Long life | - | PETRONAS Grease Clay Syn 2/220 | 
Gearbox / Reducer (oil) | AGMA 4-7 EP | High temperature High load capability Low foaming tendencies | - | - | PETRONAS Gear Syn WI
Grease points | NLGI 2 EP | High temperature Long life | - | PETRONAS Grease LiX EP 2/380 | PETRONAS Grease LiX Syn 2/220

## Slide 13: Steam Generation Plant
Draught Group - Fans
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Primary Air Fan Bearings | NLGI 2 EP | High load capability Water tolerance Long life | - | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220
Secondary Air Fan Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Forced Draught Fan Bearings (grease) | NLGI 2 EP | High load capability Water tolerance Long life | - | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220
Forced Draught Fan Bearings (oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Induced Draught Fan Bearings (grease) | NLGI 2 EP | High load capability Water tolerance Long life | - | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220
Induced Draught Fan Bearings (oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Coupling (oil) | ISO VG 46 | Oxidation stability Good air release Low foaming tendencies | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Coupling (grease) | NLGI 1 AGMA 1 and 3 | Low oil bleed Oxidation stability Resistance to centrifugal force | PETRONAS Grease Li 2 | PETRONAS Grease PE HS | -
Electric Motor Bearings (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Electric Motor Bearings (Oil) | ISO VG 32 or 46 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn

## Slide 14: Steam Generation Plant
Pre-Heater
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High load capability High temperature Long life | - | - | PETRONAS Grease LiX Syn 1/1500
Bearings (Oil in circulating system) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties |  |  | Petronas Gear Syn PAG 680
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Worm Gearbox / Reducer | AGMA 4-7 EP | High load capability Low foaming tendencies Water separability | - | - | PETRONAS Gear Syn WI

## Slide 15: Power Generation
Turbine & Generator
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Gearbox / Reducer | AGMA 4-7 EP | High load capability Low foaming tendencies Water separability | - | PETRONAS Jenteram G | -
Turbine Control System | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | - | PETRONAS Jenteram G | -
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220

## Slide 16: Voltage step up
Transformer
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Reservoir (Uninhibited) | IEC 60296 | Oxidation stability Long life | PETRONAS Elektron | - | -
Reservoir (Inhibited) | IEC 60296 | Oxidation stability Long life | PETRONAS Elektron X | - | -

## Slide 17: Water Supply - Cooling
Fans
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220

## Slide 18: Water Supply
Drum Screen Strainer / Rack Rake System
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Grease Points | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease LiX EP | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/460
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO

## Slide 19: Flue gas path and cleaning
Emission control
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High temperature Long life | - | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220

## Slide 20: Flue gas path and cleaning
Electrostatic Precipitators
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Rapper Bearings (Grease) | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSx | PETRONAS Grease LiX Syn 2/220
Electric Motor Bearings (grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAG
Grease points | NLGI 2 EP | Water tolerance High load capability High Temperature | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSx | PETRONAS Grease LiX Syn 2/220

## Slide 21: Ash Handling
Ash crusher, scraper chains
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Crusher Bearings (Grease) | NLGI 2 EP | High temperature Long life | - | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220
Chains / Sprockets | ISO VG 68 and 220 Cincinnati Machine Spec | Pumpability and sprayability Adhesive characteristics Extreme pressure | PETRONAS Slideway | - | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSx | PETRONAS Grease LiX Syn 2/220
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption | - | PETRONAS Grease LiCa TMG | 

## Slide 22: General
Blowers
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease LiX 2/170 | PETRONAS Grease LiX Syn 2/220
Gearbox / Reducer / Bearings (oil) | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 23: General
Pumps
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Oil) | ISO VG 68 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease LiX 2/170 | PETRONAS Grease LiX Syn 2/220
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 24: General
Air Compressors
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Air compressor | 51506-VDL | Oxidation stability Good air release Foam tendencies | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 25: General
Back Up Generators - Diesel & Gas Turbine
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Diesel Engine Oil | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gas Turbine | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Gearbox / Reducer | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn

## Slide 26: General
Machinery Workshops
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Cutting fluids |  | High emulsion stability Excellent lubricity and anti-weld Anti-rust, anti-corrosion Anti-sludge Anti-bacterial | Mecafluid SM 59 ** | Mecafluid S 2006 ** | -
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Hydraulics | ISO VG range HM specification | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Slide way oils | ISO VG 68 and 220 Cincinnati Machine Spec | Pumpability and sprayability Adhesive characteristics Extreme pressure | PETRONAS Slideway | - | -