## Slide 1: Power Generation
Turbine & Generator
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Gearbox / Reducer | AGMA 4-7 EP | High load capability Low foaming tendencies Water separability | - | PETRONAS Jenteram G | -
Turbine Control System | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | - | PETRONAS Jenteram G | -
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220

## Slide 2: Water Supply - Cooling
Pumps
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSx | PETRONAS Grease LiX Syn 2/220
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Electric Motor Bearings (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Electric Motor Bearings (Oil) | ISO VG 32 or 46 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Hydraulics (stationary) | ISO VG 46 / 68 High viscosity index | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV (Engen TQH 10 Series) | PETRONAS Hydraulic ESF
Gearbox / Reducer | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSx | PETRONAS Grease LiX Syn 2/220

## Slide 3: Water Supply - Cooling
Fans
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
*Petronas Gear MEP – Premium product

## Slide 4: Water Supply
Drum Screen Strainer / Rack Rake System
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Grease Points | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
*Petronas Gear MEP – Premium product

## Slide 5: General
Air Conditioners
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Refrigeration compressor | ISO 6743-3: DRA DIN 51503 | Oxidation stability Good air release Foam tendencies | - | - | PETRONAS Compressor R Syn POE OR PETRONAS Compressor R Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 6: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life Halogen free | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Engine | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling Halogen free | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability Halogen free | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption Halogen free | - | PETRONAS Grease LiCa TMG | 
Cables / Wire Ropes | OIPEEC | Core penetration Adhesive characteristics Elasticity Rust and corrosion protection Halogen free | PETRONAS Grease LiCa GEP 2.5 | - | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed Inert lubricant Halogen free | - | PETRONAS Grease PU | -
Polar Crane
Continued on next slide

## Slide 7: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Hydraulics (stationary) | ISO VG 46 / 68 | High viscosity index Water and dust tolerance Water separability Halogen free | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Hydraulics (Mobile) | SAE 10W TO-4 series | Long drain intervals High temperature handling High load capability Halogen free | PETRONAS Powertrans T4 10W | - | -
Chains / Sprockets | Spray or Grease Lubricants | Aerosol form Penetrate and have tackifier Halogen free | No product available |  | 
Slides and Rails (large quantities) | Spray or Grease Lubricants (Preserve equip) | Aerosol form Penetrate and have tackifier Solid lubricants (grease) Halogen free | No product available |  | 
Polar Crane

## Slide 8: General
Blowers
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 | Petronas Grease CaSx | PETRONAS Grease LiX Syn 2/220
Gearbox / Reducer / Bearings (oil) | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 9: General
Pumps
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Oil) | ISO VG 68 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSx | PETRONAS Grease LiX Syn 2/220
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 10: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Air compressor | 51506-VDL | Oxidation stability Good air release Foam tendencies | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Air Compressors

## Slide 11: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Diesel Engine Oil | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Gas Turbine | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Gearbox / Reducer | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Bearings (Grease) | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | -
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Back Up Generators - Diesel & Gas Turbine

## Slide 12: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Cutting fluids |  | High emulsion stability Excellent lubricity and anti-weld Anti-rust, anti-corrosion Anti-sludge Anti-bacterial | Mecafluid SM 59 ** | Mecafluid S 2006 ** | -
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Hydraulics | ISO VG range HM specification | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Slide way oils | ISO VG 68 and 220 Cincinnati Machine Spec | Pumpability and sprayability Adhesive characteristics Extreme pressure | PETRONAS Slideway | - | -
Machinery Workshops