## Slide 1: Rolling Stock
High Speed Passenger Locomotive Electric / Diesel Electric
Component Part | Lube Spec | Lube Requirements |  |  | 
 |  |  | Standard | Premium | Supreme
Alternator bearings | Polyurea Mineral or synthetic NLGI 2 | Oxidation stability Temperature control High speed | - | PETRONAS Grease PU | -
Axlebox bearings (medium speed, high load) | Lithium complex Synthetic PAO Functional additives | Oxidation stability Temperature control Mechanical stability | - | - | PETRONAS Grease LiX SYN 2/460
Axlebox bearings (high speed) | Lithium complex Synthetic PAO Functional additives | Oxidation stability Temperature control Mechanical stability | - | - | PETRONAS Grease LiX SYN 2/100
Cooling fan (grease) | Polyurea Mineral or synthetic NLGI 2 | Oxidation stability Temperature control High speed | - | PETRONAS Grease PU | -
Cooling fan (oil) | SAE 40 Mineral HDDO | Anti-wear Oxidation stability Rust and corrosion protection | PETRONAS Urania CF40 | - | -
Cooling system | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Diesel Engine (Zinc free) | 20W-40 / SAE 40 13 TBN (high sulfur fuel) 10 TBN (low sulfur fuel) | Zinc free TBN retention Proven field performance | PETRONAS Genrail V | PETRONAS Genrail VI | PETRONAS Genrail Syn VI
Diesel Engine (Zinc based) | 15W-40 | OEM approvals TBN retention Proven field performance | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E | PETRONAS Urania 7000 E 10W40 **
Continued on next slide

## Slide 2: Rolling Stock
High Speed Passenger Locomotive Electric / Diesel Electric
Component Part | Lube Spec | Lube Requirements |  |  | 
 |  |  | Standard | Premium | Supreme
Disc Brakes | Synthetic Bentone / Gel NLGI 2 | Non-melt Low friction Oil separation Oxidation stability | - | - | PETRONAS Grease LiX SYN 2/220
Exhauster / Compressor | Mineral or Synthetic | OEM approvals Oxidation stability Anti-wear | Varies according to OEM requirement | Varies according to OEM requirement | Varies according to OEM requirement
Gear coupling | Polyethylene Mineral | Anti-wear Mechanical stability Oil separation | - | PETRONAS Grease PE HS | -
Pantograph | Lithium Complex or Lithium Calcium Mineral or Synthetic Solid additives | Friction reduction Anti-wear Tackiness | PETRONAS Grease LiCa GEP 2.5 | - | -
Traction motors bearings | Polyurea Mineral or synthetic NLGI 2 | Oxidation stability Temperature control High speed | - | PETRONAS Grease PU | -
Traction motor blowers | Polyurea Mineral or synthetic NLGI 2 | Oxidation stability Temperature control High speed | - | PETRONAS Grease PU | -
Traction motors gears | Mineral or Synthetic | High load / anti-wear Oxidation stability Mechanical stability | - | PETRONAS Grease LiCa TMG | 
U-tube bearings | Lithium complex Synthetic PAO Functional additives | Oxidation stability Temperature control Mechanical stability | - | - | PETRONAS Grease LiX SYN 2/460

## Slide 3: Rolling Stock
Freight / Passenger Locomotive Electric / Diesel Electric
Component Part | Lube Spec | Lube Requirements |  |  | 
 |  |  | Standard | Premium | Supreme
Alternator bearings | Polyurea Mineral or synthetic NLGI 2 | Oxidation stability Temperature control High speed | - | PETRONAS Grease PU | -
Axlebox bearings (medium speed, high load) | Lithium complex Synthetic PAO Functional additives | Oxidation stability Temperature control Mechanical stability | - | - | PETRONAS Grease LiX SYN 2/460
Axlebox bearings (high speed) | Lithium complex Synthetic PAO Functional additives | Oxidation stability Temperature control Mechanical stability | - | - | PETRONAS Grease LiX SYN 2/100
Cardan shaft joints | Lithium complex Mineral or synthetic Functional and solid additive | Friction reduction Anti-wear Tackiness Oil separation | - | PETRONAS Grease LiX MEP | -
Cooling fan (grease) | Polyurea Mineral or synthetic NLGI 2 | Oxidation stability Temperature control High speed | - | PETRONAS Grease PU | -
Cooling fan (oil) | SAE 40 Mineral HDDO | Anti-wear Oxidation stability Rust and corrosion protection | PETRONAS Urania CF40 |  | 
Diesel Engine (Zinc free) | 20W-40 / functionalised SAE 40 13 TBN (high sulfur fuel) 10 TBN (low sulfur fuel) | Zinc free TBN retention Proven field performance | PETRONAS Genrail V | PETRONAS Genrail VI | PETRONAS Genrail Syn VI
Diesel Engine (Zinc based) | 15W-40 | OEM approvals TBN retention Proven field performance | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Continued on next slide

## Slide 4: Rolling Stock
Freight / Passenger Locomotive Electric / Diesel Electric
Component Part | Lube Spec | Lube Requirements |  |  | 
 |  |  | Standard | Premium | Supreme
Cooling system | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Exhauster / Compressor | Mineral or Synthetic | OEM approvals Oxidation stability Anti-wear | Varies according to OEM requirement | Varies according to OEM requirement | Varies according to OEM requirement
Gear coupling | Polyethylene Mineral | Anti-wear Mechanical stability Oil separation | - | PETRONAS Grease PE HS | -
Pantograph | Lithium Complex or Lithium Calcium Mineral or Synthetic Solid additives | Friction reduction Anti-wear Tackiness | PETRONAS Grease LiCa GEP 2.5 | - | -
Traction motors bearings | Polyurea Mineral or synthetic NLGI 2 | Oxidation stability Temperature control High speed | - | PETRONAS Grease PU | -
Traction motor blowers | Polyurea Mineral or synthetic NLGI 2 | Oxidation stability Temperature control High speed | - | PETRONAS Grease PU | -
Traction motors gears | Mineral or Synthetic | High load / anti-wear Oxidation stability Mechanical stability | - | PETRONAS Grease LiCa TMG | 
U-tube bearings | Lithium complex Synthetic PAO Functional additives | Oxidation stability Temperature control Mechanical stability | - | - | PETRONAS Grease LiX SYN 2/460

## Slide 5: Rolling Stock
Passengener and Freight Wagons
Component Part | Lube Spec | Lube Requirements |  |  | 
 |  |  | Standard | Premium | Supreme
Axlebox / Journal bearings (grease) | Lithium complex Synthetic PAO Functional additives | Oxidation stability Temperature control Mechanical stability | - | - | PETRONAS Grease LiX SYN 2/460
Axlebox / Journal bearings (oil) | Mineral ISO VG 57 | High load High temperature Oxidation stability | PETRONAS Circula | - | -Petronas Circula Syn
Bolts, nuts and assembly | NLGI 1 Solid additives Mineral / synthetic base oil | Anti-seize Corrosion and rust protection Oxidation stability | PETRONAS Grease LiAS | - | PETRONAS Ceramic Paste
Buffer head and coupling | NLGI 0 Bentone / Gel Synthetic | Non-melt Low friction Oil separation Oxidation stability | PETRONAS Grease LiCa GEP 2.5 |  | 
Disc brakes | Synthetic Bentone / Gel NLGI 2 | Non-melt Low friction Oil separation Oxidation stability | - | - | PETRONAS Grease Clay SYN 2/220
Doors, seals, general applications | NLGI 2 Mineral / synthetic |  | - Petronas Grease Premium 2 |  | PETRONAS Grease LiX Syn 100
HVAC (Heating Ventilation Air Conditioning) system or Refrigerated Cars | Polyol ester (POE) ISO VG 68 | Compatibility with refrigerant Low friction properties Biodegradable | - | - | PETRONAS Compressor R Syn POE

## Slide 6: Track Infrastructure
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Switches |  | Water washout Extreme temperatures Environmentally Friendly Anti-rust | No product available | No product available | No product available
Rail Curve / Flange Grease | NLGI 1 to 2 | Anti-wear Water washout Extreme temperatures Environmentally Friendly Anti-rust | - |  | -
Signals (mechanical) | NLGI EP 2 | Anti-wear Water washout Extreme temperatures Environmentally Friendly Anti-rust | PETRONAS Grease Li EP 2 | PETRONAS Grease LiX EP 2/380 | -
Track Lubrication – Track, Switches, Signals

## Slide 7: Track Infrastructure
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Catenary | NLGI EP 2 | Water washout Extreme temperatures Anti-rust Long life |  | PETRONAS Grease LiX MEP | -
Catenary / Overhead Cables

## Slide 8: Track Infrastructure
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Hydraulics | ISO VG range HM specification | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Engine | 15W-40 | OEM approvals TBN retention Proven field performance | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Gearbox | GL-5 80W-90 | High temperature Extreme pressure Anti-wear Rust prevention | PETRONAS ??? Global name | - | -
General grease points | NLGI EP 2 | Water washout Extreme temperatures Anti-rust Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease LiX EP 2/380 | -
Air compressor | 51506-VDL | Oxidation stability Good air release Foam tendencies | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn) PAO
Maintenance - Ballast Cleaning & Regulating, Material Conveying, Tamping. Dynamic Ballast Stabilising, Flash Butt Welding, Overhead Traction Equipment

## Slide 9: Secondary Services
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Cutting / Grinding fluids |  | High emulsion stability Excellent lubricity and anti-weld Anti-rust, anti-corrosion Anti-sludge Anti-bacterial | Mecafluid SM 59 ** | Mecafluid S 2006 ** | -
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 | PETRONAS Grease LiCa Semi Syn | PETRONAS Grease LiX Syn 2/220
Hydraulics | ISO VG range HM specification | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Slide way oils | ISO VG 68 and 220 Cincinnati Machine Spec | Pumpability and sprayability Adhesive characteristics Extreme pressure | PETRONAS Slideway | - | -
Air compressor | 51506-VDL | Oxidation stability Good air release Foam tendencies | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Machinery Workshops

## Slide 10: Secondary Services
Trucks and loaders
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Engine | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Transmission | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -
Converter | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -
Hydraulics / Steering | SAE 10W TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 10W ** | - | -
Hydraulics | Premium VI High VI | Water Separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Final Drive | SAE 50 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 50W ** | - | -
Grease points | NLGI 2 EP | With solid lubricants Water tolerance Tackiness High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Wheel bearing grease | NLGI 2.5 | High water tolerance High load capabilities Corrosion resistance | - | PETRONAS Tutela WB Grease | -

## Slide 11: Secondary Services
Cranes, forklifts
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Engine | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Transmission | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -
Hydraulics | Premium VI High VI | Water Separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Final Drive | SAE 50 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 50W ** | - | -
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Gearbox / Reducer | ISO VG 320 or 460 FZG Temperature range | High temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO/ PAG*
Electric motors | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Steel Ropes | OIPEEC | Core penetration Adhesive characteristics Elasticity Rust and corrosion protection | PETRONAS Grease LiCa GEP 2.5 | - | -
*Petronas Gear MEP – Premium product

## Slide 12: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Diesel Engine Oil | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Back Up Generators - Diesel