## Slide 1: Sugarcane Harvesting
Tractor
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Engine | Engine Oil 15W40 / 10W40 | Excessive dust Long periods of work Maintenance in the field | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Coolant 11 ** | PETRONAS Coolant Up ** | -
Grease Fittings | Lithium Grease NLGI 2 | Excessive dust High loads Water Contamination | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Transmission and Axle | 10W30 / GL-4 | High Loads | ARBOR MTF 10W30 ** | - | -
Gearbox / Reducer and Bearings | SAE 90/ GL-5 or 10W30 / GL-4 | High Loads | ARBOR MTF 10W30 ** | - | -
Hydraulic System | ISO VG 68 or 10W30 | Excessive dust High Temperature Water Contamination Leakage Issues | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 2: Sugarcane Harvesting
Harvester
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Engine | Engine Oil 15W40 / 10W40 | Excessive dust Long periods of work Maintenance in the field | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready | -
Grease Fittings | Lithium Grease NLGI 2 + MO2 | Water Contamination Excessive dust High loads | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Axle | SAE 85W140/ GL-5 or 10W30 / GL-4 | High Loads | ARBOR MTF 10W30 ** | - | -
Transmission | 10W30 / GL-4 | High Loads | ARBOR MTF 10W30 ** | - | -
Hydraulic System | ISO VG 68 | Excessive dust High Temperature Water Contamination Leakage Issues | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Gearbox / Reducer | ISO VG 220 with EP | High Loads | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO

## Slide 3: Sugarcane Harvesting
Truck
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Converter | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -
Engine | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready | -
Final Drive | SAE 50 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 50W ** | - | -
Grease points | NLGI 2 EP | Water tolerance High load capability OEM approvals | PETRONAS Tutela WB Grease ** |  | PETRONAS Grease LiX Syn 2/220
Hydraulics / Steering | SAE 10W TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 10W ** | - | -
Transmission | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -
5th wheel grease | NLGI 2.5 | Solid lubricants Water tolerance High load capability | PETRONAS Grease LiCa GEP 2.5 | - | -

## Slide 4: Sugarcane Receiving
Sugarcane sampling
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Hydraulic System | ISO VG 68 HLP | Water Contamination | PETRONAS Hydraulic 68 | PETRONAS Hydraulic HV 68 | PETRONAS Hydraulic 68 ESF
Electric Motor | NLGI 2 | Moisture Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 5: Sugarcane Receiving
Sugarcane Discharging
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Planetary Reduction Gear | ISO VG 460 with EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Steel Cable | Steel Cable Oil with high adhesiveness | Excessive dust Water contamination Rust and corrosion protection | PETRONAS Grease LiCa GEP 2.5 | - | -
Electric Motor | NLGI 2 | Water Contamination Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 6: Sugarcane Receiving
Feed Table
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Planetary Reduction Gear | ISO VG 460 with EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Axial bearing | Grease Lithium Complex + MO2 | Excessive dust Water Contamination Mechanical shock | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Electric Motor | NLGI 2 | Water Contamination Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 7: Sugarcane Preparation
Cane Knives
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Shaft support bearings | NLGI 2 | Water tolerance High Load capability High Vibration capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease CaSx
Turbine bearings | ISO VG | Water separability Low foam tendencies Anti wear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Gearbox / Reducer | AGMA 4-7EP | Excessive dust Med speed with high loads Water contamination | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Electric Motor | NLGI 2 | Water Contamination Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | 

## Slide 8: Sugarcane Preparation
Shredder
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Turbine and support bearings | ISO VG 68 | High load Dust contamination High Vibration | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Gearbox / Reducer | AGMA 4-7 EP | Excessive dust Med speed with high loads Water contamination | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Electric Motor | NLGI 2 | Water Contamination Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -