## Slide 1: Juice Extraction
Milling
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Mill bearings | Synthetic biodegradable oil with high viscosity (10.000 to 25.000) | Water Contamination High Loads High Temperature | Product available soon | - | -
Open Gear/ final drives | Lubricant High Viscosity with EP + Micro Pitting Resistance | Excessive dust Low speed with high loads Water contamination Medium to high temperature | Product available soon | - | -
Gearbox / Reducer | AGMA 4-7 EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Water Contamination Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 2: Juice Extraction
Diffuser
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Main drive Gearbox and bottle screw Reducers | ISO VG 460 with EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Support bearings | Grease Lithium Complex + MO2 | Excessive dust Water Contamination Mechanical shock | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Electric Motor | NLGI 2 | Water Contamination Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 3: Juice Extraction
Dewatering Mill
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Mill bearings | Synthetic biodegradable oil with high viscosity (10.000 to 25.000) | Water Contamination High Loads High Temperature | Product available soon | - | -
Open Gear/ final drives | Lubricant High Viscosity with EP + Micro Pitting Resistance | Excessive dust Low speed with high loads Water contamination Medium to high temperature | Product available soon | - | -
Gearbox / Reducer | ISO VG 320 - 680 EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Water Contamination Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 4: Juice Extraction
Conveyors
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric motor bearings | NLGI 2 | Long Life at high temperatures Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox | AGMA 4-7 EP | Good EP properties Low foam tendencies High Load capability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAG
Grease points | NLGI 2 | High load capability Water tolerance | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460

## Slide 5: Raw Sugar Production
Clarifier
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | AGMA 4-7EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 6: Raw Sugar Production
Cane Mud Filters
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Gearbox / Reducer | AGMA 4-7EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Axial bearing | Grease Lithium/Calcium NGLI 2 | Excessive dust Water Contamination Mechanical shock | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Electric Motor | NLGI 2 | Water Contamination Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 7: Raw Sugar Production
Evaporators / Pans
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Pump Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | ISO VG 220 with EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Grease points | Grease Lithium/Calcium Complex NGLI 2 with polymer | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Pump bearings Oil | ISO VG 68 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn

## Slide 8: Raw Sugar Production
Crystalliser
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | AGMA 4-7EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAG
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 9: Raw Sugar Production
Centrifugals
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease Li EP 2 | - | PETRONAS Grease LiX Syn 2/100
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 10: Raw Sugar Production
Dryer
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Fans - Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Open gears | NLGI 1-2 | High Loads High Temperature Good adhesive properties | Product available soon | - | -
Support Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | AGMA 4-7EP | Excessive dust Low speed with high loads Water contamination | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 11: Raw Sugar Production
Sorting and Storage
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | AGMA 4-7EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 12: Sugar Refining
Mingler
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | ISO VG 220 with EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 13: Sugar Refining
Centrifugals
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Hydraulic System | ISO VG 68 HLP | Water Contamination | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease Li EP 2 | - | PETRONAS Grease LiX Syn 2/100
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 14: Sugar Refining
Melter
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Hydraulic System | ISO VG 68 HLP | Water Contamination | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | ISO VG 220 with EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 15: Sugar Refining
Strainer
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | ISO VG 220 with EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 16: Sugar Refining
Carbonation Saturators
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | ISO VG 220 with EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Grease points | Grease Lithium/Calcium Complex NGLI 2 with polymer | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Pump (Oil) | ISO VG 68 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn

## Slide 17: Sugar Refining
Filtration (Rotary auto filter / Filter Press)
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | ISO VG 220 with EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 18: Sugar Refining
De-colourization
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Grease points | Grease Lithium/Calcium Complex NGLI 2 with polymer | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Pump bearings (Oil) | ISO VG 68 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn

## Slide 19: Sugar Refining
Evaporators / Pans
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | ISO VG 220 with EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Grease points | Grease Lithium/Calcium Complex NGLI 2 with polymer | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Pump (Oil) | ISO VG 68 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Compressor | DIN 51506 VDL | Oxidation stability Reduced deposits Long drain intervals | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn PAO

## Slide 20: Sugar Refining
Centrifugals
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Hydraulic System | ISO VG 68 HLP | Water Contamination High temperature Water seperatibility | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease Li EP 2 | - | PETRONAS Grease LiX Syn 2/100
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 21: Sugar Refining
Granulators
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | ISO VG 220 with EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Fans Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | PETRONAS LiX Syn 2/100

## Slide 22: Sugar Refining
Sugar Screens
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease LiX EP 2/380 | - | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | ISO VG 220 with EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 23: Sugar Refining
Packaging
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Hydraulics | Premium VI High VI | Water Separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Compressors | DIN 51506 VDL | Oxidation stability Reduced deposits Long drain intervals | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn PAO
Blowers | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn

## Slide 24: Steam/Power Generation
Boiler
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Grate Gearbox / Reducer | ISO VG 460 with EP | Excessive dust Low speed with high loads Water contamination Medium to high temperature | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAG
Grate Bearings | Grease Lithium/Calcium Complex NGLI 2 | Water Contamination High Loads High Temperature | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Electric Motor | NLGI 2 | Water Contamination Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Turbine Bearings | Turbines ISO VG 68 | Water contamination High temperature | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
FD and ID fans | NLGI 2 | High temperature Long life Environment contamination | -Petronas Grease Li EP 2 | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220

## Slide 25: Steam/Power Generation
Power Turbines
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Gearbox (if not direct drive) | Turbine oil ISO VG 68 | Water seperability High Temperature Anti wear | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Turbine | Turbine oil ISO VG 68 | Water seperability High Temperature Anti wear | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Generator Bearings | NLGI 2 | Water Contamination Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 26: Ethanol Production
Fermentation and Distillery
Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Turbine | Turbine oil ISO VG 68 | Water Contamination | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Gearbox / Reducers | ISO VG 220 with EP | Excessive dust Water contamination | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor | NLGI 2 | Water Contamination Non electricity conduction Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Pumps | ISO VG 68 | Water Contamination Anti wear | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn

## Slide 27: General
Blowers
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSx | PETRONAS Grease LiX Syn 2/220
Gearbox / Reducer / Bearings (Oil) | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 28: General
Pumps
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Oil) | ISO VG 68 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSx | PETRONAS Grease LiX Syn 2/220
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 29: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Air compressor | 51506-VDL | Oxidation stability Good air release Foam tendencies | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Air Compressors

## Slide 30: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSx | PETRONAS Grease LiX Syn 2/220
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Diesel Engine Oil | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gas Turbine | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Gearbox / Reducer | ISO VG range | Demulsibility Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Back Up Generators - Diesel & Gas Turbine

## Slide 31: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Cutting fluids |  | High emulsion stability Excellent lubricity and anti-weld Anti-rust, anti-corrosion Anti-sludge Anti-bacterial | Mecafluid SM 59** | Mecafluid S 2006 ** | -
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Hydraulics | ISO VG range HM specification | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Slide way oils | ISO VG 68 and 220 Cincinnati Machine Spec | Pumpability and sprayability Adhesive characteristics Extreme pressure | PETRONAS Slideway | - | -
Machinery Workshops