## Slide 1: Surface Mining
Dump Trucks, Wheel Loaders, Bulldozers
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Engine | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Transmission | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -
Converter | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -
Hydraulics / Steering | SAE 10W TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 10W ** | - | -
Final Drive | SAE 50 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 50W ** | - | -
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL

## Slide 2: Surface Mining
Power shovels, bucket-wheel excavators
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Engine and Generator | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Slewing gear | NLGI 2 Liebherr, Bell (white solids) | With solid lubricants Water tolerance Extreme high load capability | - | - | PETRONAS Grease LiX Semi Syn SR (Slew Ring Grease)
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Hydraulics | Premium VI High VI | Water Separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | Petronas Hydraulic ESF
Generator – Electric Motor | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Steel Ropes | OIPEEC | Core penetration Adhesive characteristics Elasticity Rust and corrosion protection | PETRONAS Grease LiCa GEP 2.5 | - | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | Gengear XEP Series | PETRONAS Gear Syn PAO
Transmission | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -
Conveyor bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220

## Slide 3: Surface Mining
Drill Rigs (blasting)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Engine | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Transmission | SAE 50 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 50W ** | - | -
Compressor | DIN 51506 VDL | Oxidation stability Reduced deposits Long drain intervals | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn
Rod thread lubricant | NLGI 1 | Solid lubricants Water tolerance High and low temperature capability Chemical corrosion resistance | PETRONAS Grease Li AS |  | PETRONAS Ceramic Paste
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Vertical bearing | NLGI 2 EP | Extreme high load Water tolerance High and low temperature capability | - | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220
Slewing ring | NLGI 2 EP | Extreme high load capability Water tolerance Solid lubricants | - |  | PETRONAS Grease LiCa MG XHL
Hydraulics | Premium VI High VI | Water Separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Drill fluid |  |  | No product available | - | -

## Slide 4: Surface Mining
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Pulley Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Compressor | DIN 51506 VDL | Oxidation stability Reduced deposits Long drain intervals | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn )
Final Drive | SAE 50 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 50W ** | - | -
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption |  | - | 
Slewing ring | NLGI 2 Liebherr, Bell (white solids) | With solid lubricants Water tolerance Extreme high load capability | - | - | PETRONAS Grease LiCa MG XHL
Cables | OIPEEC | Core penetration Adhesive characteristics Elasticity Rust and corrosion protection | PETRONAS Grease LiCa GEP 2.5 | - | -
Chains | ISO VG 220 Cincinnati Machine Spec | Tackiness Rust and corrosion protection Lubricity | PETRONAS Slideway | - | -
Torque Converter | Alstom Flender Siemens | Low foaming tendency Oxidation stability Extended drain interval | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Draglines
Continued on next slide

## Slide 5: Surface Mining
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Engine / Generator | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Gearbox / Planetaries | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Hydraulics / Steering | SAE 10W TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 10W ** | - | -
Hydraulics | Premium VI High VI | Water Separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF ()
Walking Cam |  |  | No product available |  | 
Draglines cont.

## Slide 6: Material Handling
Wheel Loaders, Bulldozers
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Engine | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Transmission | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -
Converter | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -
Hydraulics / Steering | SAE 10W TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 10W ** | - | -
Final Drive | SAE 50 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 50W ** | - | -
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL

## Slide 7: Material Handling
Stacker / Reclaimer
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption | - | PETRONAS Grease LiCa TMG | -
Cables | OIPEEC | Core penetration Adhesive characteristics Elasticity Rust and corrosion protection | PETRONAS Grease LiCa GEP 2.5 | - | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Chains | ISO VG 220 Cincinnati Machine Spec | Tackiness Rust and corrosion protection Lubricity | PETRONAS Slideway | - | -

## Slide 8: Material Handling
Collectors (Reclaimer)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption |  | PETRONAS Grease LiCa TMG | -
Cables | OIPEEC | Core penetration Adhesive characteristics Elasticity Rust and corrosion protection | PETRONAS Grease LiCa GEP 2.5 | - | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Chains | ISO VG 220 Cincinnati Machine Spec | Tackiness Rust and corrosion protection Lubricity | PETRONAS Slideway | - | -

## Slide 9: Material Handling
Trucks
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Engine | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Transmission | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -
Converter | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -
Hydraulics / Steering | SAE 10W TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 10W ** | - | -
Final Drive | SAE 50 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 50W ** | - | -
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL

## Slide 10: Material Handling
Conveyor / Pipeline
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Conveyor Back stop | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Idler rollers bearing |  |  | Filled for life - special low viscosity grease (contact OEM for initial fill) |  | 

## Slide 11: Material Handling
Railcars
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Engine (Two stroke) | SAE 40 | Cold starting Long idling periods Soot handling | PETRONAS Urania CD 40 ** | - | -
Engine (Four stroke) | 15W-40 / 10W -40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Transmission | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W ** | - | -
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Electric Motors | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Pantograph grease | NLGI 2.5 | With graphite solids Anti-wear Water tolerance | PETRONAS Grease LiCa GEP 2.5 | - | -

## Slide 12: Crushing
Gyratory Crusher (Primary Crusher)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Spider bush bearing (Grease) | NLGI 2 | High load capability High and low temperature handling Mechanical stability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Plain Bearings | AGMA 4EP | High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Spider bush bearing (Oil) | AGMA 4-7EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Gearbox / Reducer | AGMA 4EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 13: Crushing
Jaw Crusher (Primary Crusher)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Plain Bearings / Roller bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 14: Crushing
Impact Crusher (Primary Crusher)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Spider bush bearing (Grease) | NLGI 2 | High load capability High and low temperature handling Mechanical stability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Plain Bearings | AGMA 4EP | High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Spider bush bearing (Oil) | AGMA 4-7EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Gearbox / Reducer | AGMA 4EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 15: Crushing
Cone Crusher (Secondary &/or Tertiary Crusher)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Plain Bearings | AGMA 4EP | High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Spider bush bearing (Grease) | NLGI 2 | High load capability High and low temperature handling Mechanical stability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Spider bush bearing (Oil) | AGMA 4-7EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Gearbox / Reducer | AGMA 4EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 16: Crushing
Roller Crusher (Secondary &/or Tertiary Crusher)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Press bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiCa MG XHL
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Press bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Hydraulics | Premium VI High VI | Water Separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 17: Screening
Grizzly Screen / Vibrating Screen
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Hydraulics | Premium VI High VI | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | 

## Slide 18: Screening
Rotary Screen (Trommel)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Coupling | NLGI 1 AGMA CG 1 and 2 | Low oil bleed Oxidation stability Resistance to centrifugal force | PETRONAS Grease Li 2 | PETRONAS Grease PE HS | -
Idler roller bearing |  |  | Filled for life - special low viscosity grease (contact OEM for initial fill) |  | 

## Slide 19: Transfers
Conveyor
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Coupling (oil) | ISO VG 46 | Oxidation stability Good air release Low foaming tendencies | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Idler roller bearing |  |  | Filled for life - special low viscosity grease (contact OEM for initial fill) |  | 

## Slide 20: Transfers
Chutes
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220

## Slide 21: Transfers
Induction fans
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Fans (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Fans - Plain Bearings | Premium VI High VI | Water Separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 22: Transfers
Bucket Elevators
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Plummer block bearing (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO

## Slide 23: Transfers
Screw Conveyors
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Plummer block bearing (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO

## Slide 24: Transfers
Air Slides
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Fans (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 25: Grinding
Milling (Horizontal)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Plain Bearings | ISO VG Range | Water separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Circula series | - | PETRONAS Circula Syn
Slipper pad bearing (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Slipper pad bearing (Oil) | ISO VG Range | High load capability Water tolerance Long life | PETRONAS Circula series | - | PETRONAS Circula Syn
Electric Motor (Grease) | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Electric Motor (Oil) | Premium VI High VI | Water Separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Hydraulics | Premium VI High VI | Water Separability Wet and Dry Filterability Multi metal compatibility Rust and corrosion protection | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Girth Gear | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption | - | PETRONAS Grease LiCa TMG | -

## Slide 26: Pumping
Sand Pump
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Grease points | NLGI 2 EP | High load capability Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460

## Slide 27: Pumping
Slurry Pump
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Roller and Thrust Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Roller and Thrust Bearings (Grease) | NLGI 2 EP | High load capability Long life Water tolerance | - | PETRONAS Grease CaSX | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Grease points | NLGI 2 EP | High load capability Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460

## Slide 28: Classification
Spiral Classifier
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL

## Slide 29: Separation
Flotation Cells
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Vertical bearing (oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Vertical bearing (grease) | NLGI 2 EP | Extreme high load Water tolerance High and low temperature capability | - | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL

## Slide 30: Separation
Magnetic Separators
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL

## Slide 31: Separation
Launders / Clarifier
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAG
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Vertical bearing (oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Vertical bearing (grease) | NLGI 2 EP | Extreme high load Water tolerance High and low temperature capability | - | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/460
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/460
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 32: Separation
Diamond grease belt
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Recovery Grease | Cone penetration | Tackiness Penetration Congealing point | No product available yet | - | -
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAG