## Slide 1: Woodyard
Dump Truck, Wheel Loaders, Front End Loaders
Component Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Converter | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W | - | -
Engine | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Final Drive | SAE 50 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 50W ** | - | -
Grease points | NLGI 2 EP | With solid lubricants Water tolerance High load capability | PETRONAS Grease LiX MEP | PETRONAS Grease LiCa MG HL | PETRONAS Grease LiCa MG XHL
Hydraulics / Steering | SAE 10W TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 10W ** | - | -
Transmission | SAE 30 TO-4 series | Long drain intervals High temperature handling High load capability | PETRONAS Powertrans T4 30W | - | -
** Products may vary by region, check with your local PETRONAS representative

## Slide 2: Woodyard
Cranes and Lifting Equipment
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life Halogen free | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Engine | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling Halogen free | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability Halogen free | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption Halogen free |  | PETRONAS Grease LiCa TMG | 
Cables / Wire Ropes | OIPEEC | Core penetration Adhesive characteristics Elasticity Rust and corrosion protection Halogen free | PETRONAS Grease LiCa GEP 2.5 | - | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed Inert lubricant Halogen free | - | PETRONAS Grease PU | -
Continued on next slide
** Products may vary by region, check with your local PETRONAS representative
*Petronas Gear MEP – Premium product

## Slide 3: Woodyard
Cranes and Lifting Equipment cont.
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Hydraulics (stationary) | ISO VG 46 / 68 | High viscosity index Water and dust tolerance Water separability Halogen free | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF )
Hydraulics (Mobile) | SAE 10W TO-4 series | Long drain intervals High temperature handling High load capability Halogen free | PETRONAS Powertrans T4 10W ** | - | -
Chains / Sprockets | Spray or Grease Lubricants | Aerosol form Penetrate and have tackifier Halogen free | PETRONAS Slideway |  | 
Slides and Rails (large quantities) | Spray or Grease Lubricants (Preserve equip) | Aerosol form Penetrate and have tackifier Solid lubricants (grease) Halogen free | No product available (Li 000) |  | 
** Products may vary by region, check with your local PETRONAS representative

## Slide 4: Woodyard
Logging Deck and Sorter
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Bearings (Grease) | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Coupling | NLGI 1 AGMA CG 1 and 2 | Low oil bleed Oxidation stability Resistance to centrifugal force | PETRONAS Grease Li 2 | PETRONAS Grease PE HS | -
Chains |  |  | No lubrication required |  | 
Chain drive | ISO VG 68 and 220 Cincinnati Machine Spec | Pumpability and sprayability Adhesive characteristics Extreme pressure | PETRONAS Slideway | - | -
*Petronas Gear MEP – Premium product

## Slide 5: Woodyard
Debarking Drum
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption | - | PETRONAS Grease LiCa TMG | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Coupling (grease) | NLGI 1 AGMA CG 1 and 2 | Low oil bleed Oxidation stability Resistance to centrifugal force | PETRONAS Grease Li 2 | PETRONAS Grease PE HS | -
Coupling (oil) | ISO VG 46 | Oxidation stability Good air release Low foaming tendencies | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Support rolls |  | Dry lubricant required (Graphite Blocks) Can use waste lubricant (gear or hydraulic oil) | No product available |  | 
Hydraulics (stationary) | ISO VG 46 / 68 High viscosity index | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Chain drive | ISO VG 68 and 220 Cincinnati Machine Spec | Pumpability and sprayability Adhesive characteristics Extreme pressure | PETRONAS Slideway | - | -
*Petronas Gear MEP – Premium product

## Slide 6: Woodyard
Chipper
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Coupling (oil) | ISO VG 46 | Oxidation stability Good air release Low foaming tendencies | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Coupling (grease) | NLGI 1 AGMA CG 1 and 2 | Low oil bleed Oxidation stability Resistance to centrifugal force | PETRONAS Grease Li 2 | PETRONAS Grease PE HS | -
Hydraulics (stationary) | ISO VG 46 / 68 High viscosity index | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
*Petronas Gear MEP – Premium product

## Slide 7: Woodyard
Screener / Slicer
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Chains / Sprockets (CLS system) | ISO VG 68 and 220 Cincinnati Machine Spec | Pumpability and sprayability Adhesive characteristics Extreme pressure | PETRONAS Slideway | - | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
*Petronas Gear MEP – Premium product

## Slide 8: Woodyard - Transfers
Conveyor
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Couplings | NLGI 1 AGMA CG 1 and 2 | Low oil bleed Oxidation stability Resistance to centrifugal force | PETRONAS Grease Li 2 | PETRONAS Grease PE HS | -
Conveyor Back stop | NLGI 2 |  | PETRONAS Grease Li 2 | PETRONAS Grease PU | 
*Petronas Gear MEP – Premium product

## Slide 9: Woodyard
Stacker / Re-claimer
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Open Gears | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption | - | PETRONAS Grease LiCa TMG | 
Cables | OIPEEC | Core penetration Adhesive characteristics Elasticity Rust and corrosion protection | PETRONAS Grease LiCa GEP 2.5 | - | -
Hydraulics (stationary) | ISO VG 46 / 68 | High viscosity index Water and dust tolerance Water separability | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Slewing Ring Bearing | NLGI 2 | Extreme load White solids Thermal and oxidation stability | - | - | PETRONAS Grease LiX 2/600 SR
Reclaimer Chains | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
*Petronas Gear MEP – Premium product

## Slide 10: Woodyard
Pulp Chip Bins, Silos
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
*Petronas Gear MEP – Premium product

## Slide 11: Pulp Mill
Chip steaming vessel
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | - | - | PETRONAS Grease LiX Syn 1/1500
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Hydraulics (stationary) | ISO VG 46 / 68 High viscosity index | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
*Petronas Gear MEP – Premium product

## Slide 12: Pulp Mill
Pulp Digester
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | - | - | PETRONAS Grease LiX Syn 1/1500
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Hydraulics (stationary) | ISO VG 46 / 68 High viscosity index | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
*Petronas Gear MEP – Premium product

## Slide 13: Pulp Mill
Digester Blow Tanks
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
No lubrication |  |  |  |  | 

## Slide 14: Pulp Mill
Pulp Washer
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | PETRONAS Circula PM | PETRONAS Circula Syn
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Re-pulper and General Bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
*Petronas Gear MEP – Premium product

## Slide 15: Pulp Mill
Pulp Bleaching Towers
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
*Petronas Gear MEP – Premium product

## Slide 16: Pulp Mill
Screw type Pulp Press / Screw Conveyor
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
*Petronas Gear MEP – Premium product

## Slide 17: Pulp Mill
Double Belt Pulp Press
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
*Petronas Gear MEP – Premium product

## Slide 18: Stock Preparation
Pulp Storage (Pumps and Agitators)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 | Syn | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
*Petronas Gear MEP – Premium product

## Slide 19: Stock Preparation
Re-pulper
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Coupling (grease) | NLGI 1 AGMA CG 1 and 2 | Low oil bleed Oxidation stability Resistance to centrifugal force | PETRONAS Grease Li 2 | PETRONAS Grease PE HS | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
*Petronas Gear MEP – Premium product

## Slide 20: Stock Preparation
Mixing and Machine Chests
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 21: Stock Preparation
Refiners
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Geared Coupling (Grease) | NLGI 1 AGMA CG 1 and 2 | Low oil bleed Oxidation stability Resistance to centrifugal force | PETRONAS Grease Li 2 | PETRONAS Grease PE HS | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
*Petronas Gear MEP – Premium product

## Slide 22: Stock Preparation
Refined stock chest
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 23: Papermaking
Paper Machine (Wet End, Drying, Calendaring, Winding, Roll & Sheet Cutter, Conveyers (Underfloor/ Above Floor)
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Wire Roll Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/460
Press Roll Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/460
Rope Pulley Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/460
Fans – Trim (grease) | NLGI 2 | High load capability Water tolerance Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Vacuum Pumps (grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease CaSX
Rewind Stand Bearings (Pope Reel) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Calendar Roll Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | PETRONAS Circula PM | PETRONAS Circula Syn
Roll Drive Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Continued on next slide
*Petronas Gear MEP – Premium product

## Slide 24: Papermaking
Paper Machine (Wet End, Drying, Calendaring, Winding, Roll & Sheet Cutters
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Fans – Hood (grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220
Fans (oil) | ISO VG 46 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | PETRONAS Circula PM | PETRONAS Circula Syn
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Hydraulics (stationary) | ISO VG 46 / 68 High viscosity index | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Dryer Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | PETRONAS Circula PM | PETRONAS Circula Syn
Steam Rotary Joints | NLGI 2 EP Solid lubricants (Moly) | Water tolerance Antiwear properties High temperature | PETRONAS Grease LiX MEP | - | -

## Slide 25: Chemical Recovery Plant
Rotary Lime Kiln
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Girth Gear | AGMA 251.01 FZG US Steel | Pumpability and sprayability Adhesive characteristics Extreme pressure Low consumption | - | PETRONAS Grease LiCa TMG | -
Thrust Bearings | ISO VG 1000 | Lubricity High load capability Oxidation resistance Anti-wear | - | - | PETRONAS Circula Syn PAO 1000
Kiln Support Roller Bearings | ISO VG 1000 | Lubricity High load capability Oxidation resistance Anti-wear | - | - | PETRONAS Circula Syn PAO 1000
Auxiliary Diesel Engine | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Auxiliary Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor - Grease | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Drive Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP* | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Couplings | NLGI 2 EP AGMA CG 1 and 2 | Low oil bleed Oxidation stability Resistance to centrifugal force | PETRONAS Grease Li 2 | PETRONAS Grease PE HS | -
Live Ring |  |  | No Product / Graphite Powder | - | -
** Products may vary by region, check with your local PETRONAS representative
*Petronas Gear MEP – Premium product

## Slide 26: Chemical Recovery Plant
Recovery Boiler
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Forced Draught Fan Bearings (grease) | NLGI 2 EP | High load capability Water tolerance Long life | -Petronas Grease Li EP 2 | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220
Forced Draught Fan Bearings (oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Induced Draught Fan Bearings (grease) | NLGI 2 EP | High load capability Water tolerance Long life | - | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220
Induced Draught Fan Bearings (oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Circula | - | PETRONAS Circula Syn
Primary Air Fan Bearings | NLGI 2 EP | High load capability Water tolerance Long life | - | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220
Secondary Air Fan Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | PETRONAS Grease LiX Syn 2/100
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Soot blower Gearbox / Reducer | AGMA 4-7 EP | High temperature High load capability Low foaming tendencies Water separability | - | - | PETRONAS Gear Syn PAG
Precipitator Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Precipitator support bearings | NLGI 2 EP | High load capability Water tolerance Long life | - | PETRONAS Grease CaSX | PETRONAS Grease LiX Syn 2/220
*Petronas Gear MEP – Premium product

## Slide 27: Water management & treatment
Clarifiers and Filtration
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease LiX EP 2/380 |  | PETRONAS Grease LiX Syn 2/460
Gearbox / Reducer | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | - | - | PETRONAS Gear Syn WI
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Chains | ISO VG 220 Cincinnati Machine Spec | Tackiness Rust and corrosion protection Lubricity | PETRONAS Slideway | - | -
Pumps | ISO VG 68 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF

## Slide 28: Power Generation
Turbines
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Turbine bearings | ISO VG 46/68 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Turbine gear drive | ISO VG 46/68 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Pumps | ISO VG 68 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Generator bearings (grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Generator bearings (oil) | ISO VG 46/68 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn

## Slide 29: General
Blowers
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSx | PETRONAS Grease LiX Syn 2/220
Gearbox / Reducer / Bearings (oil) | AGMA 4-7 EP | Micropitting resistance High load capability Low foaming tendencies Water separability | PETRONAS Gear MEP * | PETRONAS Gear FL | PETRONAS Gear Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
*Petronas Gear MEP – Premium product

## Slide 30: General
Pumps
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Oil) | ISO VG 68 | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF )
Bearings (Grease) | NLGI 2 EP | High load capability Water tolerance Long life | PETRONAS Grease Li EP 2 | PETRONAS Grease CaSx | PETRONAS Grease LiX Syn 2/220
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -

## Slide 31: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Air compressor | 51506-VDL | Oxidation stability Good air release Foam tendencies | PETRONAS Compressor A M2 | PETRONAS Compressor A M4 | PETRONAS Compressor A Syn PAO
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Air Compressors

## Slide 32: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Bearings (Grease) | NLGI 2 EP | High load capability Extreme water tolerance Long life | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Bearings (Oil) | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Diesel Engine Oil | Engine Oil 15W40 / 10W40 | Cold starting Long idling periods Soot handling | PETRONAS Urania LD 7 ** | PETRONAS Urania 5000 E 15W40 ** | PETRONAS Urania 7000 E 10W40 **
Cooling System | Coolant Fluid | Long periods of work High temperature | PETRONAS Paraflu 11 ** | PETRONAS Paraflu Up Ready ** | -
Electric Motor Bearings | NLGI 2 | Long life at high temperature Low bleed Medium and high speed | PETRONAS Grease Li 2 | PETRONAS Grease PU | -
Gas Turbine | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Gearbox / Reducer | ISO VG range | Demulsibity Low foaming tendencies Antiwear properties | PETRONAS Jenteram | PETRONAS Jenteram G | PETRONAS Jenteram Syn
Back Up Generators - Diesel & Gas Turbine
** Products may vary by region, check with your local PETRONAS representative

## Slide 33: General
Component Part | Lube Spec | Lube Requirements | Products |  | 
 |  |  | Standard | Premium | Supreme
Cutting fluids |  | High emulsion stability Excellent lubricity and anti-weld Anti-rust, anti-corrosion Anti-sludge Anti-bacterial | Mecafluid SM 59 ** | Mecafluid S 2006 ** | -
Grease points | NLGI 2 EP | Water tolerance High load capability | PETRONAS Grease Li EP 2 |  | PETRONAS Grease LiX Syn 2/220
Hydraulics | ISO VG range HM specification | Good air release Water separability Low foaming tendencies | PETRONAS Hydraulic | PETRONAS Hydraulic HV | PETRONAS Hydraulic ESF
Slide way oils | ISO VG 68 and 220 Cincinnati Machine Spec | Pumpability and sprayability Adhesive characteristics Extreme pressure | PETRONAS Slideway | - | -
Machinery Workshops
** Products may vary by region, check with your local PETRONAS representative